TAB. 1

##### 6.1. OPERATIONAL AND TECHNICAL PARAMETERS

| Press size | 10 | 40 | 63 | Unit |
| --- | --- | --- | --- | --- |
| Version |  |  | C |  |  | C |  |  | C |  |
| Number of strokes |  |  | 80/160 |  |  | 70/140 |  |  | 65/130 | 1/min |
| Useful number of single strokes |  |  |  | 60/ - |  |  | 50/ - |  |  | 50/ - | 1/min |
|  |  |  |  | 40/ - |  |  | 35/ - |  |  | 32/ - | 1/min |
| Thickness of sheet | Single strokes |  |  | 3,2/ - |  |  | 6,4/ - |  |  | 7/ - | mm |
|  | Cont. operation |  |  | 1-1,6 |  |  | 2-3,2 |  |  | 2,5-3,5 |  |
| Maximal energy | Single strokes |  |  | 160/ - (130)/ -) |  |  | 1250/ - (1040/ -) |  |  | 2200/ - (1540/ -) | J |
|  | Cont. operation |  |  | 50-80 (50-65) |  |  | 400-630 (425-800) |  |  | 750-1100 (700-770) |  |

| Electric motor | Output |  |  | 1,1/1,5 (0,9/1,5) |  |  | 3/4 (2,5/5) |  |  | 5/7,5 (3,5/7) | kW |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Speed |  |  | 720/1450 |  |  | 710/1450 |  |  | 725/1450 | 1/min |
| Voltage | Mains | 380V, 50Hz |  |
|  | Control | 24V, 50Hz |  |
|  | Illumination | 24V, 50Hz |  |
| Compressed air | Max. pressure | 0,63 | MPa |
|  | Min. pressure | 0,5 |  |
|  | Consumption | 4 | 6 | 9 | 1/stroke |
|  | Connection | G1/2“ | G1/2“ | G1/2“ |  |
| Stopping distance ** | Slow-down angle | 17° | 40° | 43° |  |
|  | Slow-dow time | 69 | 95 | 110 | ms |
| Max. noise | Slow operation: 100 Fast operation: 100 (with used technology) | dB |

TAB. 2

##### 6.2. WORKING AND CLAMPING POSSIBILITIES OF THE PRESS

|  | kN | mm | mm |
| --- | --- | --- | --- |
| 63 | 630 | 10-105 | 70 | 315 | 335 | 355 | 800 | 25° | 800 | 630 | 280 | 250 | 45 | 315 | 350 | 300 | M24 | 400 | 20 | 170 | 200 | 50 | 60 | 40 | M12 |
| 40 | 400 | 8-95 | 60 | 265 | 295 | 300 | 800 | 30° | 660 | 530 | 225 | 200 | 45 | 265 | 370 | 120 | M20 | 360 | 15 | 170 | 200 | 50 | 60 | 40 | M12 |
| 10 | 100 | 6-65 | 45 | 165 | 225 | 180 | 800 | 30° | 450 | 320 | 135 | 120 | 36 | 160 | 240 | 70 | M12 | - | 15 | 170 | 200 | 50 | 60 | 40 | M12 |
|  |  | A | B | C | E | F | H | α | L | K | D | d | S | N | O | P | a | J | X1 | A1 | B1 | C1 | E1,F1 | G1 | a1 |
| PRESS SIZE | NOMINAL PRESS FORCE | STROKE ADJUSTABILITY | RAM ADJUSTABILITY | THROAT | GAP | PASSAGE | TABLE HEIGHT | FRAME INCLINATION | LENGTH | WIDTH | OTHER DIMENSIONS |
|  |  |  |  |  |  |  |  |  | TABLE |

TAB. 3

|  | mm | mm | mm | mm | mm |
| --- | --- | --- | --- | --- | --- |
| 63 | 610 | 85 | 220 | 200 | 20 | 83 | 248 | M12 | 200 | 83 | 200 | 110 | 160 | M12 | 20 | 450 | 280 | 140 | 220 | M20 | 50 | 85 | 40 | M24 | 220 | 22 | 38 | 16 | 27 |
| 40 | 515 | 75 | 220 | 200 | 20 | 73 | 198 | M10 | 160 | 73 | 200 | 100 | 160 | M10 | 20 | 400 | 250 | 125 | 180 | M20 | 40 | 75 | 32 | M20 | - | 22 | 38 | 16 | 27 |
| 10 | 305 | 65 | 140 | 120 | 15 | 63 | 118 | M10 | - | 63 | 120 | 70 | 100 | M10 | 15 | 280 | 180 | 90 | 140 | M16 | 40 | 75 | 32 | M20 | - | 18 | 30 | 12 | 22 |
|  | M | G | D1 | d2 | S1 | R | d1 | b | r | T | d3 | d4 | U | b | S1 | X | Y | V | Z | i | d5 | l | k | m | Z1 | e | f | g | h |
| PRESS SIZE | WIDTH | THICKNESS |  | TABLE FILLER | TABLE PLATE FILLER | LENGTH | WIDTH | OTHER DIMENSIONS | TABLE TABLE PLATE RAM |
|  | TABLE PLATE |  |  | RAM | T-SLOTS |

TAB. 4

PRESS DIMENSIONS AND FOUNDATION PLAN

|  | mm | mm | mm | kg |
| --- | --- | --- | --- | --- |
| 63 | C | 1425 | 2550 | 1790 | 1470 | 970 | 475 | 900 | 800 | 523 | 150 | 150 | 1670 | 1170 | 400 | 1100 | 250 | 850 | 160 | 110 | 110 | 320 | 85 | M30 | 170 | 1/2“ – 1835 | 5850 |
|  | P |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 5850 |
|  | R |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 5550 |
| 40 | C | 1245 | 2370 | 1585 | 1220 | 830 | 450 | 800 | 800 | 448 | 130 | 120 | 1420 | 1040 | 300 | 900 | 230 | 738 | 150 | 90 | 90 | 200 | 70 | M24 | 150 | 1/2“ – 1785 | 4500 |
|  | P |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 4500 |
|  | R |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 4250 |
| 10 | C | 970 | 1930 | 1145 | 840 | 590 | 365 | 653 | 800 | 318 | 220 | 95 | 1040 | 790 | 250 | 498 | 320 | 500 | 145 | 70 | 70 | 200 | 60 | M20 | 130 | 1/2“ – 1450 | 1250 |
|  | P |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1250 |
|  | R |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1150 |
|  | A | B | C | D | E | F | G | H | J | K | L | M | N | O | a | b | c | d | e | f | g | h | i | k | P |  |
| PRESS SIZE | VERSION | WIDTH | HEIGHT | DEPTH | OTHER DIMENSIONS | LENGTH | WIDTH | DEPTH | OTHER DIMENSIONS | AIR INLET | PRESS WEIGHT |
|  |  | DIMENSIONS OF PRESS | DIMENSIONS OF FOUNDATION |  |  |