TAB. 1

##### 6.1. OPERATIONAL AND TECHNICAL PARAMETERS

| PRESS SIZE | 25 | Unit |
| --- | --- | --- |
| EXECUTION | R | P | C |  |
| NUMBER OF STROKES | 150 | 75 | 75/155 | 1/min |
| UTILIZABLE NUMBER OF THE PARTICULAR STROKES | The clutch-brake temper. being stable | 45 | 60 | 60/45 | 1/min |
|  | Shaping off take being maximum | 45 | 60 | 60/45 | 1/min |
| METAL SHEET THICKNESS | Single strokes | 3,2 | 5 | 3,2-5 | mm |
|  | Permanent running | 1,6 | 2,5 | 1,6-2,5 |  |
| MAXIMUM WORK | Single strokes | 400 | 630 | 400-630 (400-515) | J |
|  | Permanent running | 200 | 320 | 200-320 (200-260) | J |

| ELEKTROMOTOR | Output | 3 | 2,2 | 2,2/3 (1,8/3,6) | kW |
| --- | --- | --- | --- | --- | --- |
|  | R.p.m. *** | 1420 | 710 | 725/1460 | 1/min |
| VOLTAGE | Line *** | 380V, 50Hz |  |
|  | Control | 110V, 50Hz |  |
|  | Lightening | 24V, 50Hz |  |
| PRESSURE AIR | Operating pressure | 0,6 | MPa |
|  | Working pressure | MIN. 0,5 |  |
|  | Consumed * | MAX. 0,005 | m3/zdvih |
|  | Connector | G 1/2 |  |
| BRAKING DISTANCE ** | Run down angle | 39° |  |
|  | Run down time | 85 | ms |
| MAXIMUM NOISINESS | Low-speed running: 90 | High-speed running: 100 | dB |

* Intawe volume per 1 stroke

** Clutch-brake and at nominal ari mains pressure (valve when setting-UP)

*** Standard modification

TAB. 2

##### 6.2. WORKING AND CLAMPING POSSIBILITIES OF THE PRESS

|  | kN | mm | mm |
| --- | --- | --- | --- |
| LEN 25 | 250 | 8 – 85 | 55 | 225 | 265 | 250 | 800 | 30° | 560 | 450 | 180 | 160 | 36 | 225 | 290 | 270 | M16 | 15 | 170 | 200 | 50 | 60 | 40 | M12 |
|  |  | A | B | C | E | F | H | α | L | K | D | d | S | N | O | P | a | X1 | A1 | B1 | C1 | E1,F1 | G1 | a1 |
| PRESS SIZE | NOMINAL PRESS FORCE | STROKE ADJUSTABILITY | RAM ADJUSTABILITY | GAP | GRIP | PASSAGE | TABLE HEIGHT | FRAME INCLINATION | LENGTH | WIDTH | OTHER DIMENSIONS |
|  |  |  |  |  |  |  |  |  | TABLE |

TAB. 3

|  | mm | mm | mm | mm | mm |
| --- | --- | --- | --- | --- | --- |
| LEN 25 | 435 | 65 | 180 | 160 | 20 | 63 | 158 | M10 | 63 | 160 | 90 | 125 | M10 | 20 | 355 | 220 | 110 | 180 | M20 | 40 | 75 | 32 | M20 | 18 | 30 | 12 | 22 |
|  | M | G | D1 | d2 | S1 | R | d1 | b | T | d3 | d4 | U | b | S1 | X | Y | V | Z | i | d5 | l | k | m | e | f | g | h |
| PRESS SIZE | WIDTH | THICKNESS | OTHER DIMENSIONS | TABLE FILLER | TABLE PLATE FILLER | LENGTH | WIDTH | OTHER DIMENSIONS | TABLE TABLE PLATE RAM |
|  | TABLE PLATE |  |  | RAM | T-SLOTS |

TAB. 4

PRESS DIMENSIONS AND FOUNDATION PLAN

|  | mm | mm | mm | kg |
| --- | --- | --- | --- | --- |
| LEN 25 | C | 1135 | 2145 | 1365 | 1075 | 760 | 415 | 730 | 800 | 403 | 120 | 85 | 1275 | 960 | 250 | 835 | 220 | 668 | 145 | 90 | 90 | 200 | 60 | M24 | 150 | 1/2“ – 1600 | 2500 |
|  | P |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2500 |
|  | R |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2350 |
|  | A | B | C | D | E | F | G | H | J | K | L | M | N | O | a | b | c | d | e | f | g | h | i | k | P |  |
| PRESS SIZE | VERSION | WIDTH | HEIGHT | DEPTH | OTHER DIMENSIONS | LENGTH | WIDTH | DEPTH | OTHER DIMENSIONS | AIR INLET | PRESS WEIGHT |
|  |  | DIMENSIONS OF PRESS | DIMENSIONS OF FOUNDATION |  |  |